## Slide 1: Topic 4 Energy Introduction
Thermodynamics: An Engineering Approach
8th Edition Yunus A. Çengel, Michael A. Boles
McGraw-Hill, 2015

## Slide 2
Objectives
Introduce the concept of energy and define its various forms.
Discuss the nature of internal energy.
Define specific heat and demonstrate properties for various substances.
Show relationships between internal energy, enthalpy, and specific heat.

## Slide 3: INTRODUCTION
If we take the entire room—including the air and the refrigerator (or fan)—as the system, which is an adiabatic closed system since the room is well-sealed and well-insulated, the only energy interaction involved is the electrical energy crossing the system boundary and entering the room.
As a result of the conversion of electric energy consumed by the device to heat, the room temperature will rise.
A refrigerator operating with its door open in a well-sealed and well-insulated room
A fan running in a well-sealed and well-insulated room will raise the temperature of air in the room.

## Slide 4: FORMS OF ENERGY
Energy can exist in numerous forms such as thermal, mechanical, kinetic, potential, electric, magnetic, chemical, and nuclear, and their sum constitutes the total energy, E of a system.
Thermodynamics deals only with the change of the total energy.
Macroscopic forms of energy: Those a system possesses as a whole with respect to some outside reference frame, such as kinetic and potential energies.
Microscopic forms of energy: Those related to the molecular structure of a system and the degree of the molecular activity.
Internal energy, U: The sum of all the microscopic forms of energy.
Kinetic energy, KE: The energy that a system possesses as a result of its motion relative to some reference frame.
Potential energy, PE: The energy that a system possesses as a result of its elevation in a gravitational field.

## Slide 6
Total energy of a system
Energy of a system per unit mass
Potential energy per unit mass
Kinetic energy per unit mass
Potential energy
Total energy per unit mass
Kinetic energy
Mass flow rate
Energy flow rate

## Slide 8: Example Isobutane is piped through a piping network with an inside diameter of 2 in. If the volumetric flow rate at a particular point is 225 gallons per minute (gpm), what is the mass flow rate? What is the average velocity of the fluid?
Example 1

## Slide 9: Some Physical Insight to Internal Energy
Sensible energy: The portion of the internal energy of a system associated with the kinetic energies of the molecules.
Latent energy: The internal energy associated with the phase of a system.
Chemical energy: The internal energy associated with the atomic bonds in a molecule.
Nuclear energy: The tremendous amount of energy associated with the strong bonds within the nucleus of the atom itself.
Internal = Sensible + Latent + Chemical + Nuclear
Thermal = Sensible + Latent

## Slide 10
The total energy of a system, can be contained or stored in a system, and thus can be viewed as the static forms of energy.
The forms of energy not stored in a system can be viewed as the dynamic forms of energy or as energy interactions.
The dynamic forms of energy are recognized at the system boundary as they cross it, and they represent the energy gained or lost by a system during a process.
The only two forms of energy interactions associated with a closed system are heat transfer and work.
The difference between heat transfer and work: An energy interaction is heat transfer if its driving force is a temperature difference. Otherwise it is work.

## Slide 11: More on Nuclear Energy
The best known fission reaction involves the split of the uranium atom (the U-235 isotope) into other elements and is commonly used to generate electricity in nuclear power plants (440 of them in 2004, generating 363,000 MW worldwide), to power nuclear submarines and aircraft carriers, and even to power spacecraft as well as building nuclear bombs.
Nuclear energy by fusion is released when two small nuclei combine into a larger one.
The uncontrolled fusion reaction was achieved in the early 1950s, but all the efforts since then to achieve controlled fusion by massive lasers, powerful magnetic fields, and electric currents to generate power have failed.

## Slide 12: Mechanical Energy
Mechanical energy: The form of energy that can be converted to mechanical work completely and directly by an ideal mechanical device such as an ideal turbine.
Kinetic and potential energies: The familiar forms of mechanical energy.
Mechanical energy of a flowing fluid per unit mass
Rate of mechanical energy of a flowing fluid
Mechanical energy change of a fluid during incompressible flow per unit mass
Rate of mechanical energy change of a fluid during incompressible flow

## Slide 13: Example Determine the mechanical work the pump imparts to the water.
Water
500 g/s
D1 = 3 cm
D2 = 1 cm
P1 = 100 Pa
P2 = 200 Pa
Assume z1 ≈ z2
Example 2

## Slide 16: SPECIFIC HEATS
Specific heat at constant volume, cv: The energy required to raise the temperature of the unit mass of a substance by one degree as the volume is maintained constant.
Specific heat at constant pressure, cp: The energy required to raise the temperature of the unit mass of a substance by one degree as the pressure is maintained constant.
Constant-volume and constant-pressure specific heats cv and cp
(values are for helium gas).

## Slide 17
The equations are valid for any substance undergoing any process.
cv and cp are properties.
cv is related to the changes in internal energy and cp to the changes in enthalpy.
A common unit for specific heats is kJ/kg·°C or kJ/kg·K. Are these units identical?
True or False?
cp is always greater than cv
Formal definitions of cv and cp.

## Slide 18: INTERNAL ENERGY, ENTHALPY, AND SPECIFIC HEATS OF IDEAL GASES
Joule showed using this experimental apparatus that u=u(T)
For ideal gases, u, h, cv, and cp vary with temperature only.
Internal energy and enthalpy change of an ideal gas

## Slide 19
Ideal-gas constant-pressure specific heats for some gases (see Table A–2c for cp equations).
At low pressures, all real gases approach ideal-gas behavior, and therefore their specific heats depend on temperature only.
The specific heats of real gases at low pressures are called ideal-gas specific heats, or zero-pressure specific heats, and are often denoted cp0 and cv0.
u and h data for a number of gases have been tabulated.
These tables are obtained by choosing an arbitrary reference point and performing the integrations by treating state 1 as the reference state.
In the preparation of ideal-gas tables, 0 K is chosen as the reference temperature.

## Slide 20
(kJ/kg)
Internal energy and enthalpy change when specific heat is taken constant at an average value

## Slide 21: Specific Heat Relations of Ideal Gases
The cp of an ideal gas can be determined from a knowledge of cv and R.
On a molar basis
The relationship between cp, cv and R
Specific heat ratio
The specific ratio varies with temperature, but this variation is very mild.
For monatomic gases (helium, argon, etc.), its value is essentially constant at 1.667.
Many diatomic gases, including air, have a specific heat ratio of about 1.4 at room temperature.
dh = cpdT and du = cvdT

## Slide 22
By using the tabulated u and h data. This is the easiest and most accurate way when tables are readily available.
By using the cv or cp relations (Table A-2c) as a function of temperature and performing the integrations. This is very inconvenient for hand calculations but quite desirable for computerized calculations. The results obtained are very accurate.
By using average specific heats. This is very simple and certainly very convenient when property tables are not available. The results obtained are reasonably accurate if the temperature interval is not very large.
Three ways of calculating u and h
Three ways of calculating u.

## Slide 23: Evaluation of the Δu of an Ideal Gas
Air at 300 K and 200 kPa is heated at constant pressure to 600 K. Determine the change in internal energy of air per unit mass, using
data from the air table
the functional form of the specific heat
the average specific heat value
Example 3

## Slide 24: INTERNAL ENERGY, ENTHALPY, AND SPECIFIC HEATS OF SOLIDS AND LIQUIDS
Incompressible substance: A substance whose specific volume (or density) is constant. Solids and liquids are incompressible substances.

## Slide 25: Internal Energy Changes
For small temperature intervals:

## Slide 26: Enthalpy Changes
For incompressible substances: dv = 0
For solids:
For liquids:
Constant pressure (e.g. heaters):
Constant temperature (e.g. pumps):

## Slide 27: Cooling of an Iron Block by Water
A 50-kg iron block at 80oC is dropped into an insulated tank that contains 0.5 m3 of liquid water at 25oC. Determine the temperature when thermal equilibrium is reached.
Hint: For thermal equilibrium to be reached, the sum of the changes of internal energy of the iron block and water must be equal to zero.
Example 4

## Slide 28: Enthalpy of a Compressed Liquid
Determine the enthalpy of liquid water at 100oC and 15 Mpa.
Normally, we would use the steam stables.
Table A-7
What if there was no information for this state in the Table A-7?
We approximate use saturated liquid properties in Table A-4

## Slide 29: Enthalpy of a Compressed Liquid
Determine the enthalpy of liquid water at 100oC and 15 Mpa.
What if we use the equation for a constant-temperature process?
Comparing our last two values to the exact value in Table A-7:
using saturation liquid approximation – 2.6% error
using equation for constant temp process -- ~1% error

## Slide 30: Summary
Forms of energy
  Macroscopic = kinetic + potential
  Microscopic = Internal energy (sensible + latent + chemical + nuclear)
Specific heats
  Constant-pressure specific heat, cp
  Constant-volume specific heat, cv
Internal energy, enthalpy, and specific heats of ideal gases
  Specific heat relations of ideal gases
Internal energy, enthalpy, and specific heats of incompressible substances (solids and liquids)